## Slide 1
A correct BLE stream
Advertising:
preamble: 10101010 (if the first bit of Access Address is 1 )
preamble: 01010101 (if the first bit of Access Address is 0 )
Access Address: 0x8E89BED6 (for advertising it’s a fixed pattern)
1000 1110 1000 1001 1011 1110 1101 0110
BLE Advertising packet format | BLE Data packet format (rfwireless-world.com)
So we need to find the sequence of preamble and access address after finished demodulation, to judge if it’s a BLE packet.
In theory, that is : 0101 0101 1000 1110 1000 1001 1011 1110 1101 0110
LSB

## Slide 2
Packet formats of ibeacon and Eddystone-UID in advertising channel
In general:
Preamble (1 Byte) | Access Address (4 Bytes) | PDU (2-39 Bytes) | CRC (3 Bytes)
Header (2 Bytes) | MAC address (6 Bytes) | Data (0-31 Bytes)
iBeacon prefix (9 Bytes) | Proximity UUID (16 Bytes) | Major (2 Bytes) | Minor (2 Bytes) | Tx power (2 Bytes)
Prefix data (11 Bytes) | Frame type (1 Byte) | Ranging data (1 Byte) | Namespace ID (10 Bytes) | Instance ID (6 Bytes) | Reserved (2 Bytes)
iBeacon
Eddystone-UID

## Slide 3
Eddystone-UID
2.
3.
4.
5.
I/Q waveforms
Before down sample
I/Q waveforms
Before down sample
I/Q waveforms
Before down sample
I/Q waveforms
Before down sample

## Slide 4
Eddystone-UID
Before down sample
After down sample
After down sample: 00 01010101 0110 1011 0111 1101 1001 0001 0111 0001 1111 1010
 | Preamble | Access Address | ……
00 | 01010101 | 0110 1011 0111 1101 1001 0001 0111 0001 | 1111 1010
 | 0x55 | 0x6B7D9171 | 
0x8E89BED6 == 1000 1110 1000 1001 1011 1110 1101 0110 original
0x6B7D9171 == 0110 1011 0111 1101 1001 0001 0111 0001 final
Then
So, actually